## Slide 1
Deep learning for System Identification
Introduction
Dario Piga, Dalle Molle Institute for Artificial Intelligence, Lugano, Switzerland
Lugano, April, 22nd, 2024

## Slide 2
Time | Title/Topic | Lecturer
08:45-09:00 | Welcome | 
09:00-10:30 | Introduction to Nonlinear System Identification | Dario Piga
10:30-11:00 | Break | 
11:00-12:30 | Introduction to Deep Learning | Dario Piga
12:30-14:00 | Lunch break | 
14:00-15:30 | Introduction to PyTorch | Gabriele Maroni
15:30-16:00 | Break | 
16:00-17:30 | Exercise session | Piga, Forgione, Maroni
Time | Title/Topic | Lecturer
09:00-10:30 | DynoNet- Transfer functions in deep learning (theory) | Dario Piga
10:30-11:00 | Break | 
11:00-12:30 | DynoNet- Transfer functions in deep learning (exercise) | Forgione, Piga, Maroni
12:30-14:00 | Lunch break | 
14:00-15:30 | Deep learning for state-space identification (theory) | Marco Forgione
15:30-16:00 | Break | 
16:00-17:30 | Deep learning for state-space identification (exercise) | Forgione, Piga, Maroni
Program
Day 1
Day 2
Course Duration: 16 academic hours
Preparation for the exam: 14 hours
Recognized ECTS: 1 (upon passing of the exam)

## Slide 3
Introduction to System Identification

## Slide 4
Models
Abstractions of reality
Models can describe mechanical systems, social interactions, markets, etc.
Different types of models:
  Intuitive/mental models
  Graphical models (Bode diagrams, flowcharts)
  Computer simulators (digital representation of the systems)
  Mathematical models describing relations between variables/signals of the system/process

## Slide 5
Modelling paradigms
First principles modelling (from first principles laws of physics/chemistry/biology, etc.)
  Pure physical modelling: white-box approach
  Knowledge of the physics behind the system/process
  Models are interpretable
  Sometimes, physical modelling can be complex or even impossible
Data-driven modelling (from measurements of variables gathered from experiments)
  Pure data-driven modelling: black-box approach
  Limited knowledge of the system/process
  Models are usually not explainable
  Need of (informative) data
  Generalization properties might be limited
Combination of first principles and data-driven modelling is also possible
  E.g., model structure derived from physics, and some parameters estimated from data
  In any case, even pure physical models needs often to be validated with experiments

## Slide 6
Dynamical systems
Systems with memory (present also depends on the past)
S
y
u
Described by equations in time
Continuous time: ODE
Discrete time: Recurrence equation

## Slide 7
Model structures
Model: Given past inputs and outputs, provides an estimate of the current output
  Example: ARX model
Residual signal:
  Example:
Loss:
  Example: least-squares loss:

## Slide 8
Least squares estimate: ARX model structure

## Slide 9
Example: Cascaded Tanks System
Schoukens, M. et al. "Cascaded tanks benchmark combining soft and hard nonlinearities." Workshop on nonlinear system identification benchmarks, 2016.
Fluid level control system with two tanks
Upper tank fed by a pump
Water flows from upper tank to lower tank through a small opening
Water flows from lower tank to reservoir through a small opening
Overflow in the upper tank may happen
Input: pump voltage
Output: water level of lower tank
Length of training set: 1024 samples
Length of test set: 1024 samples
Sampling time: 4 s
Metrics (over test data) both for 1-step and open-loop simulation:
Jupyter Notebook: CascadedTanksLS.ipynb (Part I)

## Slide 10
Including nonlinearities
  Linear-in-the-parameter NARX model:
  F is a vector containing (known) nonlinear elements, e.g.,
How to choose the non-linearities?
  General NARX model:
- N is a nonlinear function (e.g., neural network) of past observations
- Linearity in θ is lost

## Slide 11
Limitations of (N)ARX models
Prediction error only ``looks’’ one-step ahead
In case of data sampled at high-frequency, a good one-step ahead predictor could be:
We would like to have predictive models that provide good prediction in a long-horizon

## Slide 12
Simulation error minimization
Linear models
  OE model:
Residual signal:
Loss: sum of squared residuals is not convex anymore!

## Slide 13
First-order methods for non-convex optimization
Other updates are possible, e.g., gradient-descent with momentum:
Vanilla Gradient Descent
Jupyter Notebook: CascadedTanksLS.ipynb (Part II)

## Slide 14
Convergence of gradient-descent
Assumptions:
Convergence:

## Slide 15
Stochastic Gradient Descent
Uniformly randomly sampled from {1,2,…N}
Mini-batch gradient descent (B<<N):
Do not process the whole dataset to update the model parameters, just process a smaller batch of samples and then make the update
1 epoch = many parameter updates

## Slide 16
Deep Learning

## Slide 17
Basic units for Neural Networks
Σ
x1
x2
xd
w2
w1
wd
1
b
z
nonlinear activation function
We have a non-linear relation between inputs and outputs!

## Slide 18
Fully-connected Feedforward Neural Networks
Move from one neuron to a hierarchical structure with fully connected neurons
Input layer
Layer 2
Output layer
Layer 3
We can easily define a NARX structures parameterized by the weights (and biases) of the network

## Slide 19
FFN: PyTorch
Definition of the model class
Instantiate the model class, run and print the model

## Slide 20
Exercise description: F-16 Ground Vibration Test
Nonlinear benchmarks: https://www.nonlinearbenchmark.org/benchmarks/f-16-gvt
Ground Vibration Test of an F-16 aircraft, a key process in assessing the structural integrity and dynamic behavior of the aircraft under various conditions
Dummy payloads mounted at the wing tips.
Goal: understand how the aircraft responds to vibrations
Instrumentation: shaker was attached beneath the right wing to generate input signals, and accelerometers used to measure vibrations
Nonlinearities due to mounting interfaces of the two payloads

## Slide 21
Exercise description: F-16 Ground Vibration Test
Inputs:
  voltage measured at the output of the signal generator amplifier, acting as a reference input,
  actual force provided by the shaker and measured by an impedance head at the excitation location.
Outputs: acceleration signals measured at
  at the excitation location,
  on the right wing next to the interface,
  on the payload next to the interface
Models:
  Three independent NARX models, one for each output (optional: unique model with 3 outputs)
  Regressor for the i-th model
Performance:
  Simulation in test data (also check one-step ahead prediction)
  Metrics: RMSE and/or R2 coefficient

## Slide 22
Recurrent Neural Networks (RNNs)
Architectures tailored to process time series data and temporal information (audio, text, video, signals, etc. )
u(t)
h(t)
u(t+N)
h(t+N)
unfold
u(t)
h(t)
u(t+1)
h(t+1)
u(t+2)
h(t+2)
…
h(t-1)
or skip some initial samples

## Slide 23
Creating training data
Given an input/output sequence of length N, you can unfold the network up to N steps (you simulate N-step time ahead)
… or we can split the sequence into shorter sub-sequences (overlapped or not) of length L<<N, and thus create batch of sub-sequences. Network is unfolded for L steps (when you train, you predict L-step time ahead)

## Slide 24
u(t)
u(t+1)
u(t+2)
…
…
…
Multi-layer RNN
…
…
…
…
Hidden states of a layer are also inputs of the next layer
u(t+2)
u(t+N)

## Slide 25
u(t)
u(t+1)
u(t+2)
…
…
…
Bidirectional RNN
…
…
…
…
Causality is lost. Might not useful for prediction, but for tasks like smoothing
u(t+2)
u(t+N)

## Slide 26
Recurrent Neural Networks: Pytorch
u(t)
h(t)

## Slide 27
Recurrent Neural Networks: Pytorch

## Slide 28
LSTM: Long Short Term Memory Neural Networks
u(t)
h(t)
Image by Guillaume Chevalier, CC BY-SA 4.0, via Wikimedia Commons
Hochreiter, S., & Schmidhuber, J. (1997). Long short-term memory. Neural Computation, 9(8), 1735–1780
h(t)
c(t)

## Slide 29
Backpropagation

## Slide 30
Background: chain rule

## Slide 31
Back-propagation I
Layer 1
Layer 2
Layer 3
What we want:
Idea: Back propagate
Layer 1
Layer 2
Layer 3

## Slide 32
Back-propagation II
Focus on Layer L
Layer L
We have an interface to connect blocks/layers and recursively compute the derivatives!
Technicalities
Sigmoid activation function:
; (1- )
Linear layer: